Lab::VISA
Lab::Measurement
Instrumentation control with Perl –
The Next Generation

---
Lab::VISA is in Perl
Lab::Measurement is written in Perl
- Written in Perl (and some low-level stuff in C)
- To be used from programs written in Perl
- Perl: interpreted scripting language
- Runs on almost every OS
- Extremely good in reading data files, manipulating data, etc.
- Allows to write quick and dirty scripts that get the job done
- Also allows to write clean fullsize programs
=> ideal for experimental physics

---
Modular architecture of the core stack
measurement
… looks complicated, but:

---
Example 2
Using Lab::Measurement
#!/usr/bin/perl
use strict;
use Lab::Instrument::HP34401A;
my $hp_gpib=$ARGV[0];
print "Reading HP34401A at GPIB address $hp_gpib\n";
my $hp=new Lab::Instrument::HP34401A(
        connection_type=>'LinuxGPIB',
        gpib_address => $hp_gpib,
        gpib_board=>0,
);
my $volt=$hp->$get_voltage_dc(10,0.00001);
print "Result: $volt V\n";

---
Example 3
A real measurement!
How about doing a gate sweep, 100 steps from 0V to 1V?
#!/usr/bin/perl
use Lab::Instrument::HP34401A;
use Lab::Instrument::Yokogawa7651;
# Connect to gate voltage source
my $yoko=new Lab::Instrument::Yokogawa7651({
    connection_type => 'LinuxGPIB',
    gpib_address => 14,
    gate_protect => 0,
});
# Connect to multimeter
my $hp=new Lab::Instrument::HP34401A(0, 21);
for (my $volt=0; $volt<=1; $volt=$volt+0.01) {
    # set Yokogawa
    $yoko->set_voltage($volt);
    # wait a second
    sleep(1);
    # read multimeter
    my $vmeas=$hp->read_voltage_dc();
    # print values
    print $volt,"\t",$vmeas,"\n";
}

---
Complex measurements possible
- Not just one input, multi-dimensional measurements
- Read out as many instruments as you like, as often as you like
- Combine with monitoring of setup (pressures, temperatures, …)
- Low-level aspects (bus, connection, interface)
  - Want to access as many devices as possible
  - Linux / Windows
  - Different device drivers, different hardware interfaces
  - Thread-safe
- High-level aspects (your script, measurement)
  - Want to make measuring as comfortable as possible
  - Access different hardware with same / similar commands
  - Keep track of metadata
  - Plotting during measurement, easy re-plotting afterwards

---
High-level classes: Lab::Measurement & friends
- Provide additional tools to write better measurement scripts
- Store metadata alongside data
  - date and time
  - settings of additional instruments
  - ratio of voltage divider
  - color of the shirt you are wearing
  - everything that might be important for a later interpretation of the data
- Don‘t repeat yourself
  - Use above collected information automatically
  - Automatically plot data with correct axes, scaling, labels etc.

---
Metadata philosophy
High-level classes: metadata philosophy
Constants
R = 1000 Ω
Voltage source (Yoko)
Vbias
Columns
C1: Vbias
C2: Vresistor
unit
description…
1.5	+8.19300500E-01
1.4	+7.23413000E-01
1.3	+6.28083900E-01
1.5	+8.19300500E-01
R
V
Multimeter (HP)
Vresistor
Axes
Axis “bias voltage” (C1)
Axis “diode current”(C2 / R)
Axis “diode resistance”
(R * (C1 / C2 – 1))
unit
expression
description…
Plots
Plot “diode current”
axis “diode current” over
axis “bias voltage”
Plot “diode resistance”
axis “diode resistance” over
axis “bias voltage”
logscale
grid
ranges…

---
Example 4
Using Lab::Measurement
my $measurement=new Lab::Measurement(
    sample => $sample,
    title => $title,
    filename_base => 'zener_kennlinie',
    description => $comment,
    live_plot => 'diode current',
    constants => [
        {
        'name' => 'R',
        'value' => '1000',
        },
    ],
    columns => [
        {
        'unit' => 'V',
        'label' => 'V_{bias}',
        'description' => 'Bias Voltage',
        },
        {
        'unit' => 'V',
        'label' => 'Amplifier output',
        'description' => 'Voltage drop on serial resistor',
        }
    ],
    axes => [
        {
        'unit' => 'V',
        'expression' => '$C0',
        'label' => 'V_{bias}',
        'description' => 'Bias voltage',
        'min' => ($start_voltage < $end_voltage)
        ? $start_voltage
        : $end_voltage,
        'max' => ($start_voltage < $end_voltage)
$measurement->start_block();
for (
    my $volt = $start_voltage;
    ($volt-$end_voltage)/$step < 0.5;
    $volt += $step
) {
    $knick->set_voltage($volt);
    sleep(1);
    my $meas = $hp->get_voltage_dc(10,0.0001);
    $measurement->log_line($volt,$meas);
}
my $meta = $measurement->finish_measurement();
Run measurement!
Describe measurement!

---
Result: two files per measurement
„.dat“: your measurement data, in simple text format
# comment
# comment
x1	x2	x3	y1	y2	y3
x1	x2	x3	y1	y2	y3
...
„.meta“: all the additional metadata in computer-readable xml
- can be read out and evaluated again
- can be used to automatically replot the data for example

---
Other Lab::VISA features
Other high-level features
“Gate protect” safety mechanism
  - Makes sure that no voltage is changed to fast
  - Big voltage steps are automatically split into small, slow steps
Date/time handling
  - Date/time column can contain timestamp for every data point
  - Plot data as function of time
- Measurements with higher dimensionality
  - Each trace/sweep/line is a “block”
  - Two-dimensional plots, selections of traces, etc.

---
Utilities: plotter.pl, make_overview.pl
- plotter.pl:
  - Reads measurement file, list avaible plots (axes etc)
  - Creates postscript or pdf output
- make_overview.pl:
  - Reads all measurements e.g. in a directory
  - Generates a postscript or pdf file with plots for each measurement, including the metadata (i.e. constants, parameters, color of your shirt) (via LaTeX)
  - Great for completing your lab book

---
Modular architecture of the core stack
measurement

---
Lab::VISA architecture
Internal architecture
Divided into several layers
- Lab::Measurement is the highest abstraction layer. Provides support for writing good measurement scripts. Offers means of saving data and meta information to disk, plotting data, etc.
- Lab::Instrument package makes communication with instruments easier by silently handling the protocol involved
- Lab::Connection and Lab::Bus handle communication with the hardware and encapsulate the actual device drivers.
- The lowermost layer is given by the hardware driver and its Perl binding. Several backends are supported, e.g. NI-VISA via Lab::VISA or LinuxGPIB.

---
VISA, GPIB, etc.
VISA, GPIB, etc.
Instruments can be connected in various ways:
Serial port, GPIB, VXI, TCP/IP, USBtm, ...
GPIB (hardware and software)
  - GPIB (IEEE488): Standard by Hewlett-Packard
  - Physical layer IEEE488.1
  - Command layer IEEE488.2
  - SCPI (Standard Commands for Programmable Instruments)
VISA (software)
  - Virtual Instrument Software Architecture
  - VXI, GPIB, serial, or computer-based instruments
  - NI-VISA library is one implementation of the VISA standard
[Speaker Notes: most important for us: GPIB]

---
Open source, free software
- Open source, free software
- License: same as Perl (Artistic / GPL-2)
- Homepage: http://www.labmeasurement.de/
- Releases available from CPAN
- Development code and history on Gitorious
  https://www.gitorious.org/lab-measurement/lab
- Contributors welcome!